| Method Statement |
| --- |
| Risk Assessment/COSHH | Title |
| RA 067 | Ground Works – ride on mower |
| Resources For Activity | Ride on mower |

| Work Sequence |
| --- |
| 1. 2. 3. 4. 5. 6. 7. 8. 9. 10. 11. 12. 13. 14. 15. 16. 17. 18. 19. 20. | All operatives using Ride-On-Mowers must be trained on their safe operation and have an operator’s manual to refer to for use and maintenance purposes. All operatives to wear appropriate Personal Protective Equipment, e.g. Safety Boots, Gloves, Hard Hat, Visor, Long Sleeved Reflective Clothing, Waterproof Clothing. Appropriate Hearing Protection must also be worn. All machines must have safety checks carried out before use and defects reported to your supervisor before leaving the yard and all must be fuelled prior to start of works. Machinery must be not used where there are safety guards missing or damaged and any fuel leaks, these must be reported immediately to your supervisor. Traffic Management to be set up as per the company procedures in line Chapter 8. Check of the area to be mown and remove any objects that could damage the blades or have the potential to become a projectile whilst mowing. Ensure operator is aware of any raised iron work such as manhole covers and be especially vigilant towards surface mounted cables. Awareness of pedestrians, cyclists and other road users must be of the highest priority during any mowing operation and where members of the public could be at risk the operation must cease until it can be assessed as safe to continue. All works must be carried out in daylight hours. Care must be taken when taking ride on mowers on and off of trailers, use only trained competent operatives. Care must be taken when using the Ride-On-Mowers should they start to throw up a lot of debris. Stop and check area and rake out any surplus loose materials. On the Ferris Zero Turn only Do not use on gradients over 20º when ground conditions are wet. Do not operate on gradients over 40 º On all other mowers check the manufacturer’s recommendations for safe gradients and do not exceed these. Ensure ROPS (Roll Over Protection System) is fitted. Ensure seat belts are fitted and worn. Remove traffic management. Record details of work on Daily Work Record and pass to Supervisor. |